## Slide 1: Sendmail Performance Tuning for Large Systems
Brad Knowles
brad@shub-internet.org
http://www.shub-internet.org/
brad/papers/sendmail-tuning/
Author:
E-mail:
URL:

## Slide 2: Outline
Assumptions
Introduction
Step-by-step analysis
Implications
Things you can do
Things to avoid
Possibilities for future improvement

## Slide 3: Assumptions
Experienced *nix Administrator
Familiar with sendmail
Handle at least tens of thousands messages per day per server
Familiar with system performance tuning
  System(s) has/have already been tuned at the OS level

## Slide 4: Introduction
Focus on Transport issues
  I.e., getting large amounts of mail into and out of systems running sendmail
Will not address Local issues
  I.e., once you’ve gotten large amounts of mail into your system(s), how do you deal with it?

## Slide 5: Introduction
Transport issues
  Inbound
    Local users
    Remote users (aliased or virtual)
  Outbound
  Large mailing lists
    More properly a subset of outbound

## Slide 6: Introduction
Sendmail
  Under inetd (TCP-Wrapped?) or smap/smapd
    Suitable only for smallest of loads
      No load-average detection/handling
      Need separate queue runner process(es)
  As daemon (version ≥ 8.8)
    Can integrate with TCP-Wrappers “wraplib”
    Has “check_” anti-junkmail routines
    Version ≥ 8.9 includes additional anti-junkmail features

## Slide 7: Step-by-step Analysis: Accepting a message
Daemon
  Listens on port 25
  Accepts connection
  Forks child process
  Hands off connection
  Goes back to listening to port 25
    Alternatively, if the load average is too high, it will go to sleep for fifteen seconds and check the load average again

## Slide 8: Accepting a message
Child process
  Identifies itself
  Forks grand-child process
  Hands off connection
  Sleeps on grand-child process exit
  On return, waits for “QUIT” or “RSET” command

## Slide 9: Accepting a message
Grand-child process
  Waits for “HELO” or “EHLO” command
  Waits for “MAIL From:” command
  Creates queue files in /var/spool/mqueue
  Waits for “RCPT To:” command(s)
  Waits for “DATA” command
  Waits for “.” (on a line by itself)
  Writes the message to the mqueue
  Makes initial delivery attempt, and quits

## Slide 10: Creating queue files
Queue id based on
  Process id (pid) of grand-child
    Five digit number
  Hour of day
    Letter from A-X
  Sequence characters
    Two letters from AA-ZZ

## Slide 11: Sample queue file names
“Control” file
  qfAAA00001
“Data” file
  dfZZX32766
“Transaction” file
  tfAZL16383

## Slide 12: Creating queue files
Open “control” file with lock for exclusive writing
  If file already exists, the open w/ lock will fail, so you increase sequence by one and re-try

## Slide 13: Step-by-step analysis: Transmitting messages
Separate queue-runner process(es) started up periodically by daemon, cron, or manually
Scans entire queue directory
Calculates priority of each message
Makes delivery attempt for each message, starting with highest priority
  Each recipient domain handled in turn

## Slide 14: Transmitting messages
Alternatively, if “QueueSortOrder=host” has been set, all messages going to a particular site will be sent first, starting with the message with the highest priority to that host
  Makes maximum use of connection caching
  Good on high-speed links

## Slide 15: Transmitting messages
Finally, version 8.8 adds the option “QueueSortOrder=time”
  Intended for use only with queue-runner processes not started by sendmail

## Slide 16: Each delivery attempt
Recipient domain looked up in DNS
  All MXes identified
  Connection attempt made to each MX, until connection accepted, rejected, or list exhausted
  If multiple IP addresses for an MX, connection attempt made to each one in turn, until connection is accepted or rejected, or list exhausted

## Slide 17: Implications
System call used to open and lock files must search entire directory to ensure no other file exists with that name
  Usually a sequential search
Heavily loaded machines are more likely to still have messages in the queue with conflicting ids
Creating, opening, closing, and removing files are meta-data operations (usually synchronous)

## Slide 18: Implications
Multiple sendmail processes write incoming messages to the queue, but only one sendmail process typically handles scanning the queue and transmitting messages
  Very easy to accept messages faster than you can process them
Process to send messages is single-threaded
  A single slow site can backlog the whole system

## Slide 19: Implications
Each queue runner has to scan the entire queue before it can do anything, so as the queue grows larger and messages need to be sent out faster, it takes longer and longer for each queue runner to read in the entire queue
  There will also be more lock & directory contention
  If the load doesn’t slack off, you’ll keep slowing down more and more and more, until you stop

## Slide 20: Further implications
Lots of lock activity
Lots of meta-data activity
  E.g., directory updates
Lots of very short-lived files in queue
  Most messages (> 95%) are delivered on the first try
Lots and lots of DNS traffic

## Slide 21: Things you can do
Don’t let your /var/spool/mqueue directories grow large!
  Frequently stop sendmail, rename the queue directory/directories, create new one(s) with the same ownership & permissions, then restart sendmail
  Then run queue-runner processes in old queues to clean them out

## Slide 22: Things you can do
Put /var/spool/mqueue on a separate filesystem and write only to subdirectories
  Using mv is efficient — old directories & files can be moved and still stay on the same filesystem
  If the filesystem is unmounted, sendmail will refuse to accept messages, and they should be safely queued on the remote end
    Also avoids filling up the mqueue mount point

## Slide 23: Things you can do
Have your own “cron” job or background process that periodically fires off multiple queue runner processes
  However, this does create some additional load
    Each one will be single-threaded
    Increases lock contention
  Overall increased message throughput

## Slide 24: Things you can do
Mix QueueSortOrder=host and QueueSortOrder=time in your sets of separate queue runner jobs
  Host sorting will make maximum use of connection caching and clear out the most messages the fastest
  Time sorting will help ensure that the oldest messages get tried one more time before they might expire and bounce

## Slide 25: Things you can do
Use a different kind of filesystem for /var/spool/mqueue
  Ganger-Platt “softupdates” filesystem
    Currently, only available under *BSD
  Veritas VxFS filesystem or other JFS
  DON’T use Linux ext2fs in asynchronous mode!!!
    More on this later

## Slide 26: Things you can do
Use an OS/filesystem that has hashed directories
  System call to open and lock a file for exclusive writing will no longer have to do sequential directory searches
    E.g., SGI Irix XFS

## Slide 27: Things you can do
Dedicate nameservers, sufficient to handle the load
  Sendmail & BIND tend to fight for the same kinds of resources
    Don’t run them both on the same machine(s)
    Dedicate nameservers to the task of doing caching-only resolver service
    Shared nameservers can make better use of DNS caching for all clients

## Slide 28: Things you can do
Put /var/spool/mqueue on a faster disk subsystem
  Preferably hardware mirrored/striped (RAID 0+1) with large intelligent write-back RAM cache (battery-backed up)
  Alternatively, use solid-state disk (SSD)
  Or, do both and use Paul Pomes’“re-mqueue” script to move messages from SSD to RAID

## Slide 29: Things you can do
Run “n” sendmail daemons listening to different addresses, using separate mqueue directories
  Higher chance of avoiding lock contention
  Each queue directory can now have 1/n messages
    Smaller, can be searched faster
Set MinQueueAge to be a significant fraction of queue retry period
  Don’t waste your time retrying sites too quickly

## Slide 30: Things you can do
Choose a hardware vendor whose chip architecture handles Unix fork()/exec() calls very efficiently
  Most any of the RISC vendors
    DEC Alpha
    Sun UltraSPARC
    SGI/MIPS R10k
    Hewlett-Packard PA-8000

## Slide 31: Things you can do
Implement RAIS—Redundant Arrays of Inexpensive Servers
  Put a Network Address Translation (NAT) server or redirector in front of them, preferably one that does intelligent load-balancing
    Hardware (Holontech, Alteon, F5, etc…)
    Software (Paul Vixie’s “proxynet”)

## Slide 32: Things you can do
Large mailing lists
  Ensure that large lists are “split” into multiple smaller sub-lists, each of which can be handled by separate sendmail processes
    For Majordomo, choices are:
      Keith Moore’s “bulk_mailer”
        ftp://cs.utk.edu/pub/moore/bulk_mailer/
      Jason Tibbitts’ “TLB”
        ftp://ftp.hpc.uh.edu/pub/tlb/

## Slide 33: Things to avoid
DON’T use Linux ext2fs in asychronous mode!!!
  On a heavily loaded machine, filesystem activity (especially meta-data) is too intense to be safe
Don’t use Paul Pomes’ “re-mqueue” script to move messages around, other than from SSD to RAID
  Overhead just isn’t worth it

## Slide 34: Things to avoid
Don’t list too many MXes for your machine or domain
  All MXes will be tried sequentially, until one answers
    If the connection isn’t refused immediately, the transmitting machine will wait up to two (2) minutes before trying your next MX
    With just nine (9) MXes, this means it could take as long as eighteen (18) minutes for the sender to time out

## Slide 35: Possibilities for future improvement
Move away from standard Unix daemon fork()/exec() model
  Instead, have daemon “master” process that has pre-forked “worker” processes
Don’t create/destroy queue files
  Have a cache of queue files that get used, emptied, and returned to the pool to be used again
  Most meta-data (synchronous?) operations are avoided

## Slide 36: Possibilities for future improvement
Parallel delivery of recipients in separate domains
  Greatly improves delay from time of submission to time of receipt by last address

## Slide 37: Possibilities for future improvement
Instead of using a fixed queue retry period, instead use a TCP-style bounded exponential backoff
  If you have just tried to talk to a particular site and they were down, odds are that they will be down for a while and there’s no sense wasting your time and theirs in needlessly trying them too quickly
  Lots of real-world experience in the TCP algorithm

## Slide 38: Possibilities for future improvement
Have a separate “incoming” queue directory from the spool of messages for which at least one delivery attempt has already been made
  Avoids lock contention between new incoming mail and existing mail that is currently being processed
  Also allows for incoming queue on SSD, with long-lasting messages to be migrated to rotating media

## Slide 39: Possibilities for future improvement
Allow option to not return control to sender with “250 Ok” until message has actually been delivered, or initial delivery attempt has failed and message has been written into spool
  Allows the possibility of putting the “incoming” queue directory on a memory-based filesytem (e.g., Sun Solaris tmpfs)
    Can be much larger for much less $$$ than SSD

## Slide 40: Acknowledgement
Former employers at America Online, Inc.
Former employers & co-workers at Collective Technologies, Inc.
Eric Allman (author of sendmail), Bryan Costales (author of the book sendmail), Rob Kolstad (long-time sendmail hacker), Wietse Venema (author of TCP-Wrappers & Postfix)